## Slide 1
A SystemC-Based Implementation of an IEEE 754 Pipelined Floating-Point Unit with Zynq FPGA Verification
Ashwin Varkey
Master of Science in Computational Engineering
Department Informatik,Friedrich-Alexander-Universität Erlangen-Nürnberg
Advisor: Prof. Dr.-Ing. Dietmar Fey
June 24th 2025
Master’s Thesis Defense

## Slide 2: Outline
Motivation/Research Objectives
Architectural Design
Development Environment /Tools
Development Flow Stages
System C modelling approach
Pipeline Stages
High Level Synthesis and RTL generation
FPGA Implementation
Results
Verification
Conclusion & Future Work
Introduction

## Slide 3: Introduction
Importance of Floating-Point Units (FPUs)
  Fundamental in modern processors for accurate real-number computations.
  IEEE 754 standard ensures consistency and precision.
Custom FPU Design
  Uses RISC-V RV32F extensions for FPU pipeline (adder, multiplier, subtractor, divider)
  Faster design cycles using C/C++/SystemC and bridges gap between algorithm and hardware.
Design & Verification Methodology
  SystemC modelling → RTL design → FPGA implementation
  Custom testbenches
Target Applications
  Embedded systems with strict speed/power/resource constraints.

## Slide 4: Motivation / Objectives
Trade-offs
Balancing accuracy, latency, and resource efficiency
IEEE 754 Compliance Complexity
Managing division algorithms and special cases (NaN, infinity, denormals)
HLS to Hardware Translation
Bridging C/C++/SystemC to HDL design paradigms
Verification Coverage
Comprehensive testing across normal and edge case scenarios
FPGA Platform Integration
Managing pinout, clock frequency, and board compatibility constraints

## Slide 5: Development Environment
High-Level Modelling Environment
• C++ Compiler: GCC 9.3.0 with C++14 standard support for compilation and linking
• SystemC Library: Version 2.3.3, providing transaction-level modelling constructs and simulation kernel
RTL Design and Synthesis Tools
• Xilinx Vivado 2019.2: Primary tool for RTL synthesis, implementation, and FPGA targeting
• Intel Compiler for SystemC (ICSC): High-level synthesis tool that translates synthesizable SystemC code into System Verilog.
Verification and Analysis Tools
• GTKWave 3.3.104: Waveform visualization and signal analysis for debugging
• RISC-V GNU Toolchain: Cross-compiler and assembler for generating test programs
• Spike RISC-V ISA Simulator: Reference implementation for golden model comparison
Development Infrastructure
• Hardware Platform: Xilinx Zynq XC7Z020 evaluation board for implementation validation

## Slide 6: Development Flow Stages

## Slide 7: Architectural Design
  Handles exponent alignment, normalization, and rounding logic
IEEE 754 Single Precision Format
  32-bit implementation (1 sign, 8 exponent, 23 significand bits)
  Operations: Addition, Subtraction, Multiplication, Division
Comprehensive Standards Compliance
  Special cases: Zero, Infinity, NaN, Denormals
  Round-to-nearest (ties to even) rounding mode
  Exception handling: Overflow, Underflow, Division by Zero
Special Cases:
Zero: Exp=0, Sig=0
Denormal: Exp=0, Sig≠0
Infinity: Exp=255, Sig=0
NaN: Exp=255, Sig≠0

## Slide 8: Pipeline Stages
IF (Fetch): Retrieve instruction from memory.
ID (Decode): Decode opcode, read operands.
EX (Execute): FPU operation (add/sub/mul/div).
MEM (Memory): Pipeline buffer (minimal memory ops).
WB (Writeback): Write result to register file.
[Module] → (Ports) → [Signals] → [Processes]
↑
[Clock/Events]
[IF] → [ID] → [EX] → [MEM] → [WB] (Linked via registers/ports)

## Slide 9: Architectural Design
Pipeline Management
  External stall
  Data dependency detection with forwarding logic to minimize stalls
  IEEE 754 exception handling for overflow, underflow, and division errors

## Slide 10: Architectural Design
Register File Architecture
  32 floating-point registers (32-bit each)
  Dual-read, single-write port configuration
  Combinational reads with synchronous clock-edge writes

## Slide 11: Architectural Design
FPGA Resource Optimization
  DSP48E1 blocks for efficient arithmetic unit mapping
  BRAM utilization for register files and data buffers
  Clean clock domain management with target frequency achievement

## Slide 12: SystemC Approach
C++-Based HDL: Bridges software/hardware design.
Key Constructs:
  Modules : Hardware building blocks.
  Ports & Signals: Inter-module communication (like wires).
  Processes: Parallel "workers" (triggered by clocks/events).
  Clocks/Events: Synchronize timing (e.g., flip-flops).
Interface Definitions
- Standardized SystemC ports and signals
-Consistent communication between pipeline stages
-Facilitates modular design and verification
Process Structure
-Reset section: Initialization and configuration
-Infinite loop: Communication and computation cycles
-wait() statements: Virtual-clock boundaries for HLS optimization

## Slide 13: SystemC Approach
IEEE 754 Adder

## Slide 15: SystemC Approach
Multiplication
Sign: A_sign ^ B_sign (XOR)
Exponent: A_exp + B_exp - 127 (bias adjustment)
Mantissa: Full 24-bit multiplication
Normalization: Adjust for mantissa overflow
Rounding: Apply IEEE 754 rounding rules
Special Cases
IEEE 754 Multiplier
Non-Restoring Division Algorithm
Sign: A_sign ^ B_sign (XOR)
Exponent: A_exp - B_exp + 127 (bias adjustment)
Mantissa: Iterative 25-step division
Normalization: Adjust result format
Rounding: Apply IEEE 754 rounding rules
Special Cases: Handle division by zero

## Slide 16: SystemC Approach
Instruction Fetch (IF)
  Manages Program Counter (PC += 4).
  Reads instructions from memory.
  Terminates on dedicated halt instruction 32'hFFFFFFFF or 0
Decode Stage (ID)
  Extracts register addresses using bit masking operations
  rs1 = (instruction >> 15) & 0x1F , rs2 = (instruction >> 20) & 0x1F , rd= (instruction >> 7) & 0x1F
  Instruction decoding and parsing
  Register operand identification and retrieval
  Control signal generation
  Validity signal propagation
  Reads operands from register file (reg_file[rs1]).
Pipeline

## Slide 17: SystemC Approach
Execute Stage (EX)
  Switch statement selects FP units: 0x00 (ADD), 0x04 (SUB), 0x08 (MUL), 0x0C (DIV)
  Four dedicated floating-point units process operations
  Exception Handling
  Forwards results through result_out port
Memory Stage (MEM)
  Passthrough Role
  Propagates control signals (reg_write_out, valid_out)
  Functions as pipeline register for FP-focused design
Writeback Stage (WB)
  Updates architectural state with execution results
  Performs register write control and result validity checking
  Completes instruction execution cycle
Pipeline

## Slide 18: High-Level Synthesis and RTL Generation
Intel SystemC Compiler
  Automated SystemC to SystemVerilog translation
  Reduces manual conversion errors and development time
  Enables faster prototyping and architecture experimentation
Synthesis-Ready SystemC Design
  Synthesizable constructs: Hardware-equivalent features only
  Explicit clocking: Well-defined clock edges, no gated clocks
  Resource-aware modeling: FPGA-optimized memory/DSP usage
  Bit-accurate modeling: Defined widths, prevent overflow/underflow
Generated Verilog Structure
  Process translation: SystemC → always_comb/always_ff blocks
  Signal preservation: SystemC signals → Verilog wires/registers
  Module hierarchy: Maintained structural integrity

## Slide 19: Functional Verification Results
Comprehensive Verification Approach
  Ensures functional correctness and timing requirements
  Proper pipeline functioning (Fetch → Decode → Execute → Memory → WB)
Testbench Portability
  Equivalent test vectors for SystemC and RTL
  Edge cases: overflow, underflow, precision loss scenarios
  IEEE 754 compliance: Normal values, special cases (zero, infinity, NaN)
  Division by zero → infinity (0x7f80_0000)
RISC-V Spike Cross-Verification
  Golden reference using RISC-V ISA simulator

## Slide 20: Functional Verification Results
Waveform Analysis
  Signal propagation delays through pipeline stages
  Data flow integrity from fetch to writeback
  Floating-point arithmetic unit operation timing

## Slide 21: FPGA Implementation
FPGA Structure: Configurable Logic Blocks (CLBs) in 80×80 matrix format. Two parallel DSP48E1 SLICEs per CLB with 4× LUT-6 + 8× flip-flops
Processing System: Dual-core ARM Cortex-A9 + 28nm FPGA (2–4W power)
Implementation Steps
  Translate: Merge netlists and constraints
  Map: Assign logic to FPGA resources (LUTs, DSPs, FFs)
  Place & Route: Physical locations + interconnect establishment
  Bitstream Generation: Binary config file (.bit) successfully created using optimized DSP/logic resources for standalone PL design
Zybo Z7-20 with Xilinx Zynq-7000 SoC

## Slide 22: Conclusion
Comprehensive Development Approach
  Structured pathway: Architectural design → SystemC modeling → SystemVerilog → FPGA synthesis
Key Technical Achievements
  IEEE 754-compliant FPU
  HW-SW co-design: Resolved timing and exception handling challenges
Methodology Contributions
  SystemC-based verification: Early functional validation at high abstraction level
  Seamless HLS workflow: Automated RTL generation with reduced design cycle time
  Hybrid testing approach: Multi-level verification (C, SystemVerilog, waveforms)
  FPGA prototyping pathway: Scalable implementation for diverse platforms
Key Contributions

## Slide 23: Conclusion
Future directions to solve current limitations
Precision Support: Limited to 32-bit single precision; scope for 16-bit and 64-bit formats
Pipelining: Need to study throughput, efficiency and IPC to improve pipeline for all ISA and SIMD
The pipeline doesn't model resource conflicts (e.g., only one FP operation can execute at a time). In reality, FP units are often shared, causing stalls.
Instruction Set: Only four basic operations implemented; can extend to full RV32F instruction set. Foundation for integer operations, branching, and complex instruction sets
Performance Focus: Prioritized functional correctness over performance optimization
Verification Scope: Simulation-based testing only; formal verification methods not explored
Platform Dependency: Xilinx Zynq-specific implementation due to time constraints

## Slide 24: References
E. Oruklu, J. Hanley, S. Aslan, C. Dweik und F. Kilic, „System-on-Chip Design IEEE Computer Society, IEEE Standard for Floating-Point Arithmetic
B. Bailey, „The Evolution Of High-Level Synthesis,“ Semiconductor Engineering, Aug. 2020 (siehe S. 3).
D. Goldberg, „What Every Computer Scientist Should Know About Floating-Point Arithmetic,“ Oracle Documentation, Computing Surveys, 1991 (sieheS. 3).
M. K. Jaiswal und H. K. H. So, „Universal and Architecture-Efficient Fast Floating-Point Adder,“ IEEE Transactions on Very Large-Scale Integration (VLSI)
T. Grötker u. a., System Design with SystemC. Kluwer Academic Publishers,2002 (siehe S. 5).
M. Reshadi u. a., „Instruction Set Compiled Simulation: A Technique for Fast and Flexible Instruction Set Simulation,“ in Proceedings of the Design
Goossens,Guide to Computer Processor Architecture: A RISC-V Approach, with High-Level Synthesis (Undergraduate Topics in Computer Science) 2022.
Figures taken from https://www.cise.ufl.edu/~mssz/CompOrg/CDA-proc.html
L. H. Crockett u. a., The Zynq Book: Embedded Processing with the ARM Cortex-A9 on the Xilinx Zynq-7000 All Programmable SoC. Strathclyde
D. M. Russinoff, Formal Verification of Floating-Point Hardware Design: A Mathematical Approach. Cham, Switzerland: Springer Nature Switzerland 2019
Intel Corporation, Intel SystemC Compiler User Guide (Version 1.6.13),
S. Palnitkar, Verilog HDL: A Guide to Digital Design and Synthesis, 2nd. Prentice Hall, 2003 (siehe S. 21, 24).
Xilinx Inc., 7 Series FPGAs Data Sheet: Overview, DS180 (v2.6), Feb. 2018
Digilent Inc., Zybo Z7-20 Datasheet, 2017
Digital Circuits